## Slide 1: SMART INDIA HACKATHON 2025
Problem Statement ID – SIH25036
Problem Statement Title- Development of Sensor for Detection of Microplastics – Ministry of Earth Sciences(MoES)
Theme- Miscellaneous
PS Category- Hardware
Team ID-
Team Name- Innov8

## Slide 2: MP Detector
MP Detector
We process water samples through a dark chamber with controlled illumination. A multispectral sensor and camera capture spectral and image data, which are analyzed by an AI model to detect and classify microplastics. If abnormal levels are found, the system logs results and alerts the monitoring team via a mobile app.
Innov8
PROBLEM STATEMENT
Expected Solution:
A portable battery powered sensor system
Detecting & classifying Microplastics
Fast results with minimal sample prep
Water Inlet
Pre-Filtering
Flow Cuvette/ Membrane
UV Light
AS7265x
Spectrometer
ESP32-S3
TinyML
Model
Dark Chamber
Li-ion 18650 cells
Voltage Regulator
Power Management
Wi-Fi
Mobile App
Data Visualization
User Interface
Database

## Slide 3: TECHNICAL APPROACH
Firmware: C++ (ESP-IDF)
ML models:
  1D-CNN — input 18 channels → Conv(32, kernel=3) → Conv(64) → Dense(64) → Softmax (polymer classes). ~10k params.
  Tiny CNN on cropped particle images (quantized to int8).
Backend: Python backend (training), Flutter mobile app
DB: Firebase
HARDWARE & OPTICS
Optical layout: Dark chamber, 3–5 mm flow cuvette or membrane holder, UV/blue LED (365–405 nm).
Sensors: AS7265x multispectral (18 bands 410–940 nm) for spectral signature; ESP32-S3 camera (5 MP) with 10× objective for ≤50 µm resolution.
Electronics: ESP32-S3 devboard, LED driver (PWM), I²C for AS7265x, 12V Li-ion battery + buck regulator (5V/3.3V rails).
SOFTWARE & ML
Innov8

## Slide 4: TECHNICAL APPROACH
Innov8

## Slide 5: FEASIBILITY AND VIABILITY
Feasibility
Low-cost hardware components
Prototype is practical
Performance can be enhanced with a 10× objective
Challenges:
Environmental noise (algae, silt) complicates microplastic detection
Staining agents like Nile red may produce False positives
Strategies:
Stable energy source
Quality tested components
Continuous data logging & updates
Innov8

## Slide 6: IMPACT AND BENEFITS
Benefits:
Fast, low-cost field screening of water bodies
Minimal operational cost
User-friendly Interface
Remote Data logging & Visualization
Highly scalable
Impacts on Environment:
Early detection enables timely intervention and cleanup prioritization
Helps maintain a safe food chain
Innov8

## Slide 7: RESEARCH AND REFERENCES
References:
Stressor-AOP: https://cb.imsc.res.in/saopadditives/
NOAA NCEI Marine DB: https://pmc.ncbi.nlm.nih.gov/articles/PMC10589325/
Marine Debris Program: https://marinedebris.noaa.gov/
Overview of Analytical methods for the determination of microplastics: https://www.sciencedirect.com/science/article/abs/pii/S0165993623003485
Methods of Microplastic Detection by Bree Foster
Estimated Cost:
ESP32-S3 : ~2000
OV5640 : ~2500
AS7265x : ~9000
UV LED torch (365–395 nm) : ~1000
Battery Li-ion(12v 5Ah) : ~1500
Total: 18000
Innov8